## Slide 1: Closing the data gap on 4,000 bank branches
PORTFOLIO ENERGY REVIEW
Electricity, Scope 2 emissions, and where the savings are
Nilima Gurjar · Synthetic portfolio case study · 2026
42%
of portfolio electricity
was never on a bill
Notes: Today I'm walking through a portfolio electricity and Scope 2 assessment for a 4,000-branch bank network. The headline: 42% of the portfolio's electricity wasn't on a bill we had, so the real work was estimating that gap in a way we can defend. The data is synthetic, built to mirror the gaps real portfolios have.

## Slide 2: 314 GWh, 117k tCO₂, and 150 branches to target first
314 GWh
Portfolio electricity
58% metered, 42% estimated with tested methods
~117k tCO₂
Location-based Scope 2
eGRID2022 U.S. average factor
25.6 GWh
Savings potential
Half of it sits in just 150 branches
Recommendation Audit the top 150 branches first, and replace electric-resistance heating at end of equipment life.
Notes: If you remember three numbers: 314 gigawatt-hours of electricity, about 117,000 tonnes of location-based Scope 2, and 25.6 gigawatt-hours of savings potential, half of which sits in 150 branches. My ask is to start audits there.

## Slide 3: Only half the branches report a full year of electricity
Problem statement
Leadership needs a portfolio electricity and Scope 2 number it can defend to auditors and investors.
But 47% of branches have partial or no meter data, because the landlord pays, the meter is shared, or the site is unmetered.
Summing the bills would undercount the portfolio by about 42%.
Chart: Branches by electricity data coverage
| Complete (12 mo) | Partial (3–8 mo) | No meter data
Branches | 2108 | 810 | 1082
Notes: The business problem: we need a number we can defend. Only 2,108 of 4,000 branches have a full year of data. 810 have a few months, and 1,082 have nothing, mostly because the landlord pays or the meter is shared. Just adding up bills undercounts by about 42%.

## Slide 4: Four questions shaped the analysis
1
How big is the data gap, and where is it?
Coverage by branch, data tier, and fuel
2
Are the anomalies errors or real behavior?
Zero readings, outliers, duplicates
3
How do we fill gaps in a way we can defend?
Methods tested against known answers
4
What drives electricity intensity, and where are the savings?
Drivers, gap to peers, concentration
Notes: I framed four questions before touching the data. How big is the gap. Are the strange readings errors or real. How do we fill gaps defensibly. And what drives intensity, which is where savings come from.

## Slide 5: Five steps from raw bills to a ranked savings list
1
Profile
Map coverage by branch and data tier
SQL
2
Quality check
Test zeros, outliers, and duplicates
SQL
3
Annualize
Scale partial years by state seasonality; backtest
SQL · window fns
4
Model
Regression for unmetered branches; 5-fold CV
Python · statsmodels
5
Roll up & rank
Totals, Scope 2, gap to format median
SQL + Python
Inputs 4,000 branches · 50,312 monthly records · 5 fuel types · 12 months (2025) · EPA eGRID2022
Notes: Five steps. Everything except the regression runs in SQL on DuckDB, so the pipeline is transparent and reproducible. The regression is in Python with statsmodels, validated with cross-validation in scikit-learn.

## Slide 6: The anomalies were real behavior, not bad data
202
zero-kWh months
All at 30 net-metered solar sites. Solar covered demand, so the readings are valid.
11 of 14
intensity outliers
Small drive-thru branches, where kWh per sq ft runs high by design.
So what Deleting these rows would have biased the baseline. Every exclusion rule is documented in SQL.
Notes: A common mistake is to delete anything that looks odd. The 202 zero months were all at solar sites, so they're real. And 11 of the 14 outliers were tiny drive-thru branches. Keeping them was the right call.

## Slide 7: Each gap-filling method beat its simple alternative
Chart: Median absolute error (%)
| Partial-year branches | Unmetered branches
Simple alternative | 4.6 | 17.7
Chosen method | 2.1 | 12.3
Partial-year branches
Seasonal scaling vs. linear, backtested on 2,047 complete branches. Linear misses that a partial year without summer understates use.
Unmetered branches
Regression (R² = 0.72) vs. a format-median benchmark, 5-fold cross-validation.
Notes: This is the slide that makes the number defensible. I tested each method against branches where we know the answer. Seasonal scaling halved the error on partial years. The regression beat the simple benchmark by about five points.

## Slide 8: Portfolio electricity totals 314 GWh, 42% of it estimated
Chart: 
| Metered | Annualized | Modeled
GWh | 181.2 | 63.3 | 69.7
314
GWh total
~117,000 tCO₂
Location-based Scope 2, using the eGRID2022 U.S. average factor (823 lb CO₂/MWh)
Metered: 2,108 branches with full-year bills
Annualized: 810 branches, seasonal scaling
Modeled: 1,082 branches, regression
Notes: The total is 314 gigawatt-hours. 181 is metered, 63 is annualized from partial years, and 70 is modeled. At the national average grid factor that's roughly 117,000 tonnes of CO2. Before external reporting I'd switch to subregion factors.

## Slide 9: Electric-resistance heat is the biggest intensity driver
Chart: Median electricity intensity by HVAC type (kWh/sq ft/yr)
| Gas boiler + split AC | Gas rooftop unit | Gas furnace + split AC | Heat pump | Host building system | Electric-resistance RTU
kWh/sq ft | 17.9 | 18.2 | 18.4 | 26.1 | 27.5 | 31.7
+58%
kWh/sq ft vs. gas-heat rooftop units, controlling for size, format, hours, and state
Read with care: electric-heated sites move heating from gas onto the meter. Heat pumps do this efficiently; resistance heat does not.
Notes: HVAC type explains more variation than anything else in the model. Electric-resistance rooftop units use 58% more electricity per square foot than gas-heated ones, after controls. The caveat matters: this is an electricity view. Heat pumps look high because they carry the heating load, but they're efficient. Resistance heat is the real target.

## Slide 10: Half the savings sit in just 150 branches
Chart: Share of 25.6 GWh savings, by branch rank
| Top 150 | 151–250 | 251–500 | 501–1,054
Share | 50.2 | 15.4 | 21.6 | 12.8
Who the top 150 are
12.8 GWh
of savings at 4% of branches
83%
electrically heated (heat pump or resistance)
79%
full-service format
Notes: Savings are the gap between each branch and the median for its format. 1,054 branches are above median, but the top 150 hold half the savings. They're mostly electrically heated full-service branches, which gives us a clear profile to target.

## Slide 11
Recommended next steps
1
Audit the top 150 branches
12.8 GWh of savings concentrated in 4% of the portfolio
2
Replace electric-resistance heat
Swap to heat pumps at end of equipment life
3
Close the data gap
Request landlord data for the 1,082 unmetered branches
4
Refine Scope 2 before reporting
Move to eGRID subregion factors
Notes: Four asks. Start audits at the top 150. Plan heat pump replacements for resistance heat as equipment ages. Chase landlord data, because every metered branch shrinks the estimated share. And refine emission factors before anything goes in an external report.

## Slide 12: Tools used, and what to keep in mind
SQL (DuckDB)
Profiling, QC, window-function annualization, backtesting, savings ranking
Python
statsmodels regression, scikit-learn cross-validation, pandas
GitHub
Reproducible pipeline: one command regenerates every number
Limitations
Synthetic data: findings demonstrate the method, not real bank behavior
One national emission factor; subregion factors would shift tCO₂
12 unmetered solar branches modeled at gross, not net, use
Electricity-only view; total energy would include gas
Notes: Tools: SQL on DuckDB for the data work, Python for modeling, all in a public GitHub repo. And the limitations I'd want any decision-maker to know before acting.